set routing-instances cbec.com instance-type virtual-router
set routing-instances cbec.com access address-assignment pool POOL-1 family inet network 10.21.2.0/26
set routing-instances cbec.com access address-assignment pool POOL-1 family inet range r1 low 10.21.2.2
set routing-instances cbec.com access address-assignment pool POOL-1 family inet range r1 high 10.21.2.62
set routing-instances cbec.com access address-protection
set routing-instances cbec.com interface xe-4/2/0.3715  ß----------interface value need to update from uplink properties
set routing-instances cbec.com interface lo0.149  ß------------------ loopback value need to fetch from property file
set routing-instances cbec.com routing-options static route 0.0.0.0/0 next-hop 192.168.181.138  ß--------neighbour ip address
set routing-instances cbec.com routing-options aggregate route 10.21.2.0/26
set routing-instances cbec.com routing-options autonomous-system 65103  ß---Need to update AS number from properties file
set routing-instances cbec.com protocols bgp group cbec.com type external
set routing-instances cbec.com protocols bgp group cbec.com import cbec.com_import
set routing-instances cbec.com protocols bgp group cbec.com export cbec.com_export
set routing-instances cbec.com protocols bgp group cbec.com peer-as 9829
set routing-instances cbec.com protocols bgp group cbec.com neighbor 192.168.181.138   ß--------neighbour ip address

cbec.com:-

Context Value-

POOL-1:-

inside context, next string of 'interface' is the value of ri_name-pool, it may be multiple strings.

10.21.2.0/26:-

inside context, below string 'interface', next string of 'ip address', it would be again multiple as per the ri_name-pool

low 10.21.2.2
first IP of ri_address_pool

high 10.21.2.62
max IP of ri_address_pool

xe-4/2/0
uplink_interface	find string 'UPLINK-01 <context>', than find 'port ethernet' string above it, and than take the string next to 'port' i.e. for e.g. 'ethernet 3/4'
Note: find string 'UPLINK-02' and so on and repeat same process and create parameter e.g. uplink_interfce_01, uplink_interface_02 and so on.

uplink_unit_no	find string 'UPLINK-01 <context>', than find 'dot1q pvc' string above it, and than take the string next to it.
Note: find string 'UPLINK-02' and so on and repeat same process and create parameter e.g. uplink_unit_01, uplink_unit_02 and so on.

uplink_vlan_id	same as uplink_unit_no

wan_ip_address	find string 'interface UPLINK-01' inside context, find string 'ip address' below and take the next string as wan_ip_address_0 and wan_ip_address_1 as per the repetive values of 'interfcae UPLINK-02' in same context.

lo0.149	take value from Loopback details sheet table

192.168.181.138   neighbour ip address
in side context, find string 'neighbor' and next to next string 'external', so between the string is 'neighbor_ip_address' value

65103  --Need to update AS number from properties file
in side context, find 'router bgp' next string value is 'bng_as_no'